## Slide 1: Trishuli Flood Mapping — 2026
Sentinel-1 SAR + Machine Learning
P1 · P2 · P3 · P4
2026-10-01

## Slide 2: Problem
• Trishuli / Bhote Koshi corridor flooding
• Need rapid extent + impact mapping
• 48-hour SAR-to-decision pipeline

## Slide 3: Data
• Sentinel-1 GRD (VV/VH) — 30 m
• Copernicus DEM — 30 m
• OpenStreetMap buildings & roads

## Slide 4: Method
1. Align DEM + S1 to 30 m UTM grid
2. Detect flood: Δ VV < -1.5 dB
3. Train XGBoost on 9 features
4. Overlay on OSM for impact

## Slide 5: Flood Detection (P2)
• 22.66 km² observed flooded
• Threshold -1.5 dB (clamped Otsu)
• Slope & permanent water masked

## Slide 6: Susceptibility Model (P3)
• XGBoost, 9 features
• AUC 0.998
• Predicted 23.11 km² — 1.02× observed

## Slide 7: Validation
• F1 ~0.91
• IoU ~0.84
• 90%+ of observed flood captured

## Slide 8: Impact (P1)
• Buildings flooded: <FILL IN>
• Road segments affected: <FILL IN>
• Cut-off settlements: <FILL IN>

## Slide 9: Deliverables
• flood_dashboard_full.html
• flood_model.joblib
• FINAL_REPORT.pdf
• Reproducible pipeline on GitHub

## Slide 10: Limitations & Next Steps
• Single-event training
• 30 m misses sub-pixel urban flooding
• Next: dual-orbit fusion, S2 validation